Termite Management.                                                      Section 2

When buying a house

It is strongly recommended that before you buy a house, you have an expert inspect it for termite activity. The cost of a full report is minimal compared with the potential expense of repairs. Ensure you engage a properly qualified, experienced and insured pest inspector and ask them to report on the type, age and condition of any termite barrier system which may be installed, and on the materials used for critical structural elements.

Long-term protection

Protection in the long-term can be gained by the application of chemical or physical barriers (or both) to prevent termites from penetrating the structure. An Australian Standard (AS3660.1)

has been written on the subject. The aim is to keep any cellulose material, especially timber away from soil contact and to encourage termites to build a mud tube out in the open where it can be seen during a regular, careful inspection.

Termite barriers are designed to stop concealed access and force termites into the open where their mud tunnels can be more easily detected. Physical barriers range from small graded stone particles to fine termite-resistant, stainless steel mesh and chemically impregnated composite products.

Termite resistant materials are designed to protect the critical concealed structural elements of your home, while ensuring a ‘small target’ for any termite activity and do not become less effective over time. Ensure you use a product that has been certified and complies with the relevant Australian Standard.

You must be proactive in your decision-making process. And most importantly, you must arrange for appropriately qualified operators to carry out regular inspections. You should also be fully informed about ongoing maintenance requirements and the best pre or post construction options.

How do I identify termite activity?

Termite activity is often difficult to detect as it usually occurs in concealed areas. It is recommended to conduct regular visual inspections in and around you home to identify any potential termite activity. If you suspect any termite activity you should engage an expert to conduct a full inspection.

Image 1	Image 2

What to look for:

·	Weak timber that breaks easily revealing wafer thin layers

(see image 1). Skirting boards are often the first point of damage.

·	Look for changes in corner facias under gutters as termites are

attracted to damp or moist areas.

·	Mud-like tubes or material around external footings/brickwork, or

internal fittings like service pipes and electrical plugs (see image 2).

·	Cracks/holes in timber or plaster with a fine dust residue.

·	Check surrounding trees, wood piles and garden beds (up to a

50 metres radius around the home) to identify if a colony is

active nearby.

What should I do if I find termites?

Should you uncover termites, try to put things back as they were. Surface spraying and ripping out floorboards, architraves or other building material may kill a few termites in those timbers but in doing so you have lessened the chances of an expert effectively treating the main nest. The termites will re-group and probably choose to attack another section of the house structure.Depending on preferences and construction, an approved pest controller can assist with the best type of treatment, which, besides chemical spray options, may include reticulation and/or baiting systems.

Termites regularly re-infest with multiple nests attached to the colony at a radius of 50 plus metres. This, together with the fact that a termite colony can consist of over two and a half million individuals, means that if you do discover an infestation, it is prudent and civically responsible to immediately notify your neighbours and local council.

Useful Contacts

CSIRO enquiries

Bag 10

Clayton South VIC 3169 Telephone: 1300 363 400 Fax: 95452175

Email: enquiries@csiro.au www.csiro.au

Australian Environmental Pest Managers Association

Suite 4, 532-542 Hampton Street Hampton Victoria 3188 Australia Telephone: (03) 9597 0664 Fax: (03) 9597 0669

Email: info@aepma.com.au www.aepma.com.au

Useful Contacts

CSIRO enquiries

Bag 10

Clayton South VIC 3169 Telephone: 1300 363 400 Fax: 95452175

Email: enquiries@csiro.au www.csiro.au

Australian Environmental Pest Managers Association

Suite 4, 532-542 Hampton Street Hampton Victoria 3188 Australia Telephone: (03) 9597 0664 Fax: (03) 9597 0669

Email: info@aepma.com.au www.aepma.com.au

Tips

Avoiding damage by termites

·	Choose a termite management system to suit your preferences and the needs for the type of construction.

·	Investigate the total cost of termite management systems over the lifetime of your home.

·	Understand the system of termite management and maintenance requirements for your house.

·	Have a pest controller inspect the house every 12 months, especially if you are in a high hazard area. An expert inspection should also be done before purchasing a property with a termite free statutory declaration provided by the vendor.

·	If you are concerned about existing or potential infestation, you should contact your local pest management company.

Maintenance/housekeeping

·	Check your property and building regularly for termite activity to reduce the risk of damage.

·	Plumbing leaks, drainage problems and roof leaks should be

addressed promptly, as termites are attracted to damp conditions.

·	Garden beds and mulching should not be built up against walls,

as this allows termites an undetectable entry point to the building.

·	Do not block or cover sub-floor ventilation with garden beds,

mulching or paving.

·	Do not stack materials against walls, as this can allow termites to enter without early detection.

·	Sub-floor areas should be well ventilated. Ensure vents are not obstructed.

·	Storage of cellulose products in the sub floor space should be avoided.

·	Use termite resistant timber for works around the property, including retaining walls.

·	Use metal stirrups for verandah and gateposts.

·	Clean and check timber decks regularly.